# Tender text for presence detectors

# Presence detector thePrema P360 Slave FM WH / GR

Passive-infrared presence detector for ceiling installation; square 360° detection range, walking 100 m2 (10 x 10 m), seated 64 m2 (8 x 8 m)  at 3.5 m installation height;

Operating voltage 230 V AC / 50 Hz; Protection rating IP 20, in fitted state IP 40;

Configurable sensitivity; ready for operation immediately thanks to factory presets; can be configured remotely with remote control; test mode to check function and detection area; extension of detection area by master/slave or master/master switch;

Installation depth 40 mm, ceiling installation in flush-mount socket or ceiling installation socket 73A, ceiling installation possible with surface-mount frame;

Manufacturer: thebenHTS

Type: thePrema P360 Slave FM.. (can only be used with thePrema P360-100 FM.. as master)

Order no.: 2070030 (thePrema P360 Slave FM WH, white)

2070031 (thePrema P360 Slave FM GR, grey)

Unit: ST

### Accessories

### "SendoPro 868-A" management remote control

Optional

For the installer for start-up or adjustment to usage conditions.

Text-based operator guidance in the display. Transmission of individual settings or complete configuration sets to the detector possible. Suitable for all remote controlled thebenHTS presence detectors.

Order No.: 9070675

### Service remote control "theSenda P"

Optional

Order no.: 9070910

### Surface mount frame 110A WH

Optional

Order no.: 9070912

### Ceiling installation socket 73A

Optional

Drill diameter 73 mm

Order no.: 9070917